## Slide 1: EGH450 Advanced Unmanned Aircraft Systems Tutorial 02 Airframe, Power/Propulsion and Payload
Felipe Gonzalez - felipe.gonzalez@qut.edu.au
Kye Morton– morton9@qut.edu.au
Science and Engineering

## Slide 2: Reminders
S901 Access – Please attend one of the orientations with Steve Bulmer held in this week or in Week 3. Check Blackboard announcement for induction times.
UAV Collection- UAV are ready for collection in S9 store. Please contact Steve Bulmer or Kye if there are any issues with this.
Ordering Parts– If any group has not received an ordered item/s please check the store and email Kye.
Science and Engineering

## Slide 3: Airframe

## Slide 4: Airframe Subsystem Info
This subsystem is responsible for design, development and modification of the airframe structure.
The construction of the airframe for the all the UAVs should be complete at this stage however additional modification maybe be required, for example
  Payload Mounts
  Camera/gimbal Attachments
  VICON Tracking Marker Attachments
  Weight and Payload Balancing
Mounting Plates designs are available on QUTAS/Wiki
  Link - https://github.com/qutas/info/tree/master/Schematics
Science and Engineering

## Slide 5: Airframe Subsystem Info
  Vicon IR Marker Attachment
    Crucial for tracking the UAV within the test area, if any move and fall off during flight can cause inaccurate position tracking from VICON system.
    You can use double sided tape available at Da Vinci however it is recommend that
    Recommended to modify airframe to attach marker M4 bolts
    Ensure the marker holds are symmetrically placed around the airframe
  Ensure the camera mounts are attached by week 6
    Allows you to do a live test during week 6 at Da Vinci and record a bag file with video for testing outside of practicals.
Science and Engineering

## Slide 6: Power and Propulsion

## Slide 7: POW/PRO Subsystem Info
  Your role in the team is to ensure all the systems that require power is distributed accordingly from the battery
    Provide Regulated 3.3v-5v lines for the O/B computes, Servo/Solenoids, Autopilot
    Make sure the BEC is rated to handle the load required
    It is your job to understand what each subsystems' power requirements are and the type of connection and method of distribution.
      For example a Rpi can be given 5V power using either Micro USB or Servo connector
  Reminder that you may be required to do additional thrust testing at the practicals from week 3.
    Please contact Kye so he can bring the thrust test rig down
Science and Engineering

## Slide 8: POW/PRO Subsystem Info
  Most of this subsystem is complete, however you may need to modify changes as the other subsystems develop.
    Motors, ECS, and Autopilot are already installed
  Document the connections and provide a final power distribution schematic for final demonstration and submission.
Science and Engineering

## Slide 9: POW/PRO Subsystem Info
Cable Management
  Zip ties are your friend, please ensure there are no loose cables as this is very hazardous during flight
  High Gauge cable for motor/esc, ensure any soldered cables/connectors are insulated with heat shrink
  A neat system is much easier to debug than a messy one.
Tutor will come around and check whether you need rearrange wiring and secure to the frame.
Science and Engineering

## Slide 10: PAYLOAD

## Slide 11: Payload Subsystem Info
  “When each marker is identified and localised, the UAVUSR must immediately deploy the correct simulated medication” - HLO 5 Medication Delivery
Science and Engineering

## Slide 12: Payload Subsystem Info
  Your role in the team is to the payload is to accurately delivered when the specific target is detected
    Design and mechanism to drop a right package to the right target
    Make sure you test the accuracy and precision of your delivery
Science and Engineering

## Slide 13: Payload Subsystem Info
  Week 9 Demonstration
      This is only a bench test but must be electronically activated but no involvement to the actual mechanism.
      You may activate the mechanism using the following- ROS control node, electronic switch, basic pi script
      Recommended that you use ROS control node as this will be needed in the final demo
  Week 12 Final Demonstration
      Fully autonomous operation so you should already be integrating the system the UAV by week 9.
Science and Engineering

## Slide 14: Payload Subsystem Info
  Interfacing with others subsystem
    You will be required to write a ROS node/s to control/activate you mechanisation when target are detected and localised.
    Servo based Payloads delivery
      Can use onboard computer -PIGPIO/wiringpi, http://abyz.me.uk/rpi/pigpio/ Odroids- https://wiki.odroid.com/odroid-xu4/application_note/gpio/wiringpi
      Can also use autopilot(mavros) as the hardware interface(very simple)
    Solenoid based Payloads delivery
      Must use onboard computer -PIGPIO/wiringpi, http://abyz.me.uk/rpi/pigpio/ Odroids- https://wiki.odroid.com/odroid-xu4/application_note/gpio/wiringpi
  Reminder that 3D printing of your system may take up to 3 weeks, especially toward the latter end of the semester
    Please complete your mechanical design early in the semester to allow time for modification and possible troubleshooting.
    3D Printing can be done at the Launchpad in O Block
Science and Engineering